San Angelo School District Network Wiring Specifications

(Gigaspeed, Fiber Optic, Video, and Telephone Cabling)

Revised July 21, 2004

1.	Cabling Standards

a.	Install, label, and test  (plenum or non-plenum-rated for above ceiling locations depending on local fire codes and ventilation systems) , Gigaspeed Ethernet (1000BaseT) unshielded twisted pair (UTP), 24 AWG 4 pair wire, in each class room and one (1) near each persons desk in administrative areas.  The wiring is to be home run from each station location marked building plans.  With a patch panel on the wall, mounted cable rack in the appropriate wiring closet.  All wiring will be a complete Avaya, Orthonics or Leviton solution.

b.	Cables will be terminated in the Patch Panel in a sequential order by room number or location.  The only exception would be when a new cable is added to an existing patch panel and the next consecutive location is taken.  In this case the next available empty jack will be used.

c.	Designate each as follows:  Wiring Closet Termination Point, Room, Drop, Position, and Jack ID Label (Sample shown below). This information will be recorded and the data provided to the district.

Example:

Closet		Room		Drop	Position	Length         Jack ID

B121		B122		1	2		75	         122,1,2

d.	All work will be done in accordance to Category 6 specifications as published in TIA/EIA standards 568, 568-A, 569, 570, 606, and 607 and applicable standards for 1000BaseT.  Additions are listed in TSB31, 36, and 40 and The National Electric Code for low voltage wiring.  BICSI Telecommunications Standards will be considered as the standard for all installation practices.   In addition, all installation will be compliant with ISDN BRI (ISO 8877). Cable connectors shall meet IEEE 802.3i specifications.  All Jacks will be wired in accordance with the TIA/EIA 568-B wiring method.

e.	If any fire rated wall is penetrated it must be sealed to maintain the fire rating that existed prior to the penetration.  All interior or exterior wall penetrations will be appropriately sealed.  Interior wall penetration will, at the minimum, be sealed with fire resistant, insulating foam.  Exterior penetrations will be sealed with cement, metal, calking, or foam where appropriate.

f. 	Avaya Giga Speed Cabling, The term  Giga Speed is an Avaya product

term to identify the Avaya cable rated at a  sum of 1.2 ghz over four pairs. This cable meets "proposed" category 6 draft submitted to the EIA /TIA committee. This cable is stamped on the sheath with "5E" until the ratification of the standard by EIA /TIA.  Installed cables are tested at 5E level until ratification of the draft.  The Avaya Power Sum cable is rated at a sum of 622 mhz over four pairs.  This is also stamped 5E on the sheath.  Both cables are covered under the Avaya Systimax program and warranted for 25 years for performance.

2.	Conduit and Cable Bends

a.	If running cables "bare", or on cable trays, cables must be plenum rated if required by local fire codes.

b.	Neatness in cabling, ensuring that all cables are  "hidden" from open view or run in wall mounted raceway, is mandatory.  Floor area runs are to be avoided.  Cables shall not be stapled to walls, abutments, supports, or any other objects.  Concurrent data cable runs shall be bundled together neatly and loosely.

3.	Wiring Drop and Connector Specifications

a.	Each wiring drop will include: as a minimum a single port wall plate with one (1) terminated cable.  One (1) gigaspeed cable per plate terminated and tested.  Multiple drops can be installed in the same box with multi port face plates when the drops will be in close proximity to each other.

b.	Each four pair, 24 AWG gigaspeed cable will be terminated in an eight pin, modular jack at the work area.  These connectors shall be  UTP outlets, which meet all criteria, listed in TIA/EIA 568.

4.	Wiring Description for Horizontal Cabling

a.	All wiring cables with a run length of 295 feet or under shall consist of 24 AWG plastic insulated conductors formed into four twisted pairs and enclosed by a plastic jacket. Cabling will be plenum rated (if required by local fire codes).  The manufacturer to be certified as Gigaspeed compliant shall rate all cables.

b.	The wire O.D. of the cable shall be no less than .18 and no more than .22 trade size.

c.	The pair assembly shall meet the color code according to TIA/EIA 568, section 10.2.1.1.3.

d.	No wire can be bent tightly  (i.e., greater than 6 x O.D. of the cable) or kinked at the jack.

e.	All cables must be tested at least once and shall perform better than the minimum requirements as outlined in TIA/EIA 568-A (including appendices) as it pertains to gigaspeed cabling.

f.	Any cable that fails to meet testing measurements will be completely re-run at the vendor's expense including equipment, parts, and time.

g.	All horizontal data cabling will be yellow or blue.

h.	Cable lengths are to be recorded using cable test equipment and the data provided to the School District.

i.  	All cabling when terminated will be untwisted the minimum distance necessary to make the connection.  At no time should the untwisted strands exceed maximum length recommended by the EIA/TIA and BICSI standards.

5.	Electrical Considerations

a.	All wires must be run per the following standoff distance table:

Condition				<2kVA	2.5kVA	>5kVA

Unshielded power lines or electrical	 5 inches	12 inches	24 inches

equipment in proximity to open or  non metal

pathways

Unshielded power lines or electrical	 2.5 inches	6 inches	12 inches

equipment in proximity to a grounded metal

conduit pathway

Power lines enclosed in a grounded metal	3 inches	6 inches

conduit in proximity to a grounded metal

conduit pathway

b.	All wires must be run at least 6.5 feet from any electromagnetic field, such as those generated by electrical motors, converters and invertors.

c.	All wires must be run at least 6 inches distant from fluorescent lights.

d.	All wires must be run at least 1 foot from FAX machines, refrigerators, microwaves, and copiers.

e.	No data jack will be located under a chalkboard if at all possible.

6.	Wiring Closets (Technology Closet)

a.	The wiring closets are transition points between the horizontal distribution pathways and the backbone or part of the backbone itself.

b.	The wiring closets are to contain one or more floor, wall or ceiling mounted jack strips.  The placement will be (7) to more than (8) feet above the floor.  There will be one RJ-45 connector per cable.  There will also be a 110 Volt AC receptacle located adjacent to each jack strip.

7.  	Patch Panels (Connecting Hardware)

a.	The transmission properties of the internally wired connecting devices shall meet or exceed the transmission performance requirements specified in TIA/EIA 568, 	section 12.2.6.2, and the NEC, interfaces included.

b.	Standard interface jacks and plugs shall meet the requirements of TIA/EIA-TSB-31, Ref B 1.37.

c.	Interface jacks shall be eight pin jacks with pin/pair assignments according to the 568A designation with applicable color code combinations.  These pin/pair assignments are compatible with ISDN BRI (ISO 8877), Ref B1.24.  Wiring will be terminated with the TIA/EIA 568B wiring method.

d.	All cable will be sequentially installed according to the room number or location number.

8.	Wiring Labels and Wiring Management

a.	Labeling all wall jacks, cables, patch cables and patch panel jacks is mandatory.  The method for applying labels will be left to the discretion of the installer; however the District will be supplied with a sample for approval prior to any installations.  Labels will be of some indelible ink, non-removable, tape or under a plastic retaining strip which is part of the faceplate or jack strip.

b.	The labels themselves shall be in accordance with the description given in this document.

9.	Testing

a.	All cable testing shall be performed at least once by the installation vendor and the resulting data provided to the district.

b.	All cables shall be tested by a certified, calibrated scanner according to an accepted and approved gigaspeed test procedure as noted in TIA/EIA 568-A.

c.	Any cable runs that fail to meet specifications in the bid and that fail the scanner test shall be completely rerun at the expense of the vendor.

d. 	All cables that are rerun will be tested for compliance as if they were an initial run.  The results of these tests shall be treated the same as described above.

10.  Conduit and Raceways

a.  All wiring which cannot be installed in the walls or ceiling will be enclosed in surface mounted raceway.

b.  Any wiring, which must extend through an outdoors area must be in conduit.

11.  Cabling will never be laid directly on the ceiling grid.  It will be suspended above the

Ceiling grid on Avaya approved J hooks or equivalent when ever possible.

12.  Cabling will not be attached to existing cabling, plumbing, water pipes, air ducts, ceiling

supports or electrical or communications conduit.

13.  There will be one drop cable (White), and one patch cable, (blue) supplied for each cable

installed between a room and the patch panel.

Fiber Optic Cabling

a. All standards mentioned above for installation apply except those that are specifically for copper wiring.  Fiber optic cable shall be certified to meet or exceed the current American National Standards Institute (ANSI) Fiber Distributed Data Interface (FDDI) specification.

b.  Cabling will be a minimum of six strand indoor/outdoor cable, multimode, 62.5/125 microns plenum or PVC according to local fire codes.

c.  All terminations will be with ST type ceramic or stainless connectors, glued not crimped.

d.  All cable will terminate in and San Angelo ISD approved distribution enclosure, such as South Hills Datacomm enclosure, Part No. 36358P.

e.  The enclosure will be populated with sufficient ST to ST bulkhead adapters, such

as South Hill Datacomm Part No. 1003P, so that each fiber is  connected to an

adapter.

f.  All fiber optic cable installations will be certified with and approved fiber optic certification tester and written results of testing supplied to San Angelo ISD.   For multimode fibers, testing will be done at both 850 and 1300nm, using LED sources.

g. The installed fiber cable should have at least 10 feet of coiled slack cable at each end to allow for repair and relocation.

h. Cabling will be plenum or non-plenum depending on local fire codes and ventilation system requirements.

i.    Interduct - All exposed fiber optic cabling interior to a building, or where deemed appropriate on the interior to a building, will be in interduct.

j.  Conduit - All exposed fiber optic cabling exterior to a building will be installed

in conduit from the point of egress from the building.

k. This cable shall be suitable for installation free-air, in building Risers, in Conduit, in Cable Tray and/or in interduct.

l. Cable Materials shall be all dielectric (no conductive materials).

m. Outer Sheath: The Outer Sheath shall be marked with the manufacturer's name, date of manufacture, fiber type, flame rating, UL symbol, and sequential length markings every two feet.

n. Temperature Range:

Storage:	-40 to +70 C (no irreversible change in attenuation)

Operating:	-20 to +70 C (OFNP)

o. Humidity Range:  0 to 100%

p. Max. Tensile Load ( 12-fibers; Backbone, Riser, Intra-building)

10.0.10 During Installation:	1332 Newton’s (300 lb. force) (no irreversible change in attenuation).

Long Term:	600 N (135 lb. force)

q. Bending Radius:

During Installation:	20 times cable diameter

No Load:		10 times cable diameter.

r. Multimode Optical Fiber Specifications - Backbone Cabling

All optical fibers shall be sufficiently free of surface imperfections and inclusions to meet the optical, mechanical, and environmental requirements of this specification. Factory optical fiber splices are not allowed.

s. All fibers shall have been subjected to a minimum tensile proof test by the fiber manufacturer equivalent to 100-kpsi.

t. All fibers in each cable shall be guaranteed to meet the San Angelo Independent School District’s specifications.

u. Multi-mode Fiber cables shall be sized as needed.

v. Multi-mode Optical Fibers in each cable shall meet the following specifications:

Fiber Type:  Multi-mode; doped silica core surrounded by a concentric

glass cladding.

Index Profile:	Graded Index

Transmission Windows:	850-nm and 1300-nm

Core Diameter: (nom)	50.-m (microns)  3

Cladding Diameter:	125-m  2

Core-clad Concentricity:	  3-m

Cladding Non-circularity	  2.0%

Fiber Coating Diameter	250-m  15 (primary coating)

900-m (nominal) Secondary coating (tight buffer)

All coatings shall be mechanically strippable without damaging the optical fiber.

Attenuation (max. @ 235 C; Backbone) @  850-nm	3.75-dB/km @ 1300-nm

w. When tested in accordance with FOTP-3, "Procedure to Measure Temperature Cycling Effects on Optical Fibers, Optical Cable, and Other Passive Fiber Optic Components", the average change in attenuation over the rated temperature range of the cable shall not exceed 0.50 dB/km with 80% of the measured fibers not exceeding 0.25 dB/km.

Bandwidth (min.) @  850-nm	160-MHz*km @ 1300-nm	500     “

No multi-mode optical fiber shall show a point discontinuity greater than 0.2 dB at the specified wavelengths. Such a discontinuity or any discontinuity showing a reflection at that point shall be cause for rejection of that fiber by the Owner.

Product:  Commscope, Berk-Tek, or equivalent (plenum)

x.  All fiber optic cable will be installed in accordance with SAISD Wiring Standards (attached) and within BICSI code allowances.

y. All new fiber optic cable will be installed in interduct in the ceiling and in the tunnel system and buried conduits when exterior and not aerial.

z. All strands will be terminated in a lockable metal box as specified in the SAISD Wiring Standards or a lockable fiber optic assembly in the equipment rack.co-located in lockable data cabinet.

aa. All new fibers will be terminated with SC connectors.

bb.  If different length or termination connectors are needed for the fiber optic patch cables the vendor will supply them.

Warranty

Installed cabling (walls, ceiling, under floor) will be warranted for a period of 20 years.  Wall jacks, and patch panels must be warranted for a period of 20 years.

Video Cable Wiring

Classroom

1.  All cable to the classroom will be RG-6 non-plenum or plenum rated cable depending of local fire codes.

2.  All cables from the classroom will be home run to a wiring closet room (some structures have  sub distribution rooms).

3.  Cables be terminated with “F” Type connectors on either end.

4.   All terminations will be in a front corner of the room mounted just below the ceiling as specified in the floor plans and mounted in a standard cable face plate.

5.   There will be a duplex 110 Volt AC receptacle installed adjacent to each cable outlet jack.  If possible the AC outlet and the cable jack should be in the same face plate.

6.  Provide a 24 inch pigtail at each outlet terminated with an AF@ connector on each end.

7.  The signal strength in each classroom should be no less than 0db.

Wiring Closet

7.  All terminations in the wiring closet will be mounted to a passive splitter to provide easy connectivity to the video cable coming from the main video (Audio-Video).

8.  A pathway will be provided from the wiring closet to the main building (Audio-Video) where the commercial cable is terminated.

9.  Cable connectivity from the wiring closet to the main video distribution room will be of sufficient capacity (2 inch coax) to insure adequate signal strength to the closet.

10.  If  the signal strength at the wiring closet is not sufficient then an amplifier must be installed to boost the signal strength for a strength of 0db at the classroom termination.

11.  A duplex 110 AC outlet will be mounted near the cable termination panel in the wiring closet.

Main Video Cable Termination Room

12.  The setup in this room (Audio-Video room) will allow a commercial television cable (TCA) vendor to connect their signal into the Lincoln video system.

13.  The installation will also allow the connection of the Channel 1 video system to the Lincoln video system. The vendor/vendors will supply all equipment necessary to insure proper operation of their signal across the Lincoln video system.

14.  The 2 coax from each sub distribution room will be terminated in the main video room and connected to amplifiers with directional taps to distribute the signal to each pod (A, B, C, and D).

Telephone Cable Wiring

- Each data wall plate in every classroom will also contain a telephone jack wired back to a patch panel located in the same closet as the jack strip for the network wiring.  Wiring will  be of the same standard as the data cabling and terminated in the room with the same  data jack as the data wiring.  Wiring marked for voice use will be of a different color (preferably white).

Patch Cable Standards

1.  Patch Cables (patch panel to the data switches) should be - 1 foot long - White - for the panels in the RE-4 cabinets

2.  Patch Cables for the Wireless Access Points  (patch panel to the data switches) - 1 feet long - Green - for the panels in the RE-4 cabinets

3.  Patch Cables (patch panel to the data switches) should be - 3 foot long - White - for the other cabinets and the MC

4.  Patch Cables for the Wireless Access Points  (patch panel to the data switches) - 3 feet long - Green - for the other cabinets and the MC

5.  Drop Cables (from the wall jack to the computers) -  15 feet long - Gray

6.  Drop Cable for WAP (faceplate to WAP) - 1 foot long - Gray

7.  Video coax pigtails to TV from the Jack - 24 inches - Black

8.  Telephone cable from phone to the wall jack - standard length and color

9.  We'll be using 48 port switches which have very little room between jack ports, so please do not order and cables with boots over the jacks.